## Slide 1
NETWORKING FUNDAMENTALS
OSI Reference Model
Understanding how data travels across seven layers, from the physical wire to the user's application.

## Slide 2
OVERVIEW
What is the OSI Model?
A reference model describing how information from a software application on one computer moves through a physical medium to the software application on another computer.
Consists of seven layers — each performs a particular network function.
Developed by the International Organization for Standardization (ISO) in 1984.
Divides the whole communication task into seven smaller, manageable, self-contained tasks.
Application
Presentation
Session
Transport
Network
Data Link
Physical
02

## Slide 3
CHARACTERISTICS
Two Groups of Responsibility
Each layer is self-contained, so the OSI model splits neatly into layers handled by the host and layers handled by the network.
Responsibility
of the Host
Application
Presentation
Session
Transport
Responsibility
of the Network
Network
Data Link
Physical
Upper Layers
Handle applications using software; closest to the user.
Lower Layers
Manage data transfer using hardware and software; the physical layer connects to cables and sends data.
03

## Slide 4
THE STACK
The 7 Layers of the OSI Model
7
Application
Provides services to the user.
6
Presentation
Translation, compression & encryption.
5
Session
Establishes, manages & terminates sessions.
4
Transport
Reliable message delivery, process to process.
3
Network
Moves packets from source to destination.
2
Data Link
Error-free transfer of data frames.
1
Physical
Physical medium through which bits are transmitted.
04

## Slide 5
1
LAYER 1 OF 7
Physical Layer
L2 data
(from Data Link)
→
Physical Layer
converts to signal
→
10101000000010
(raw bits)
Main Points
Sends raw data (0s and 1s) over cables or wireless.
Deals with hardware like cables, switches, and network cards.
Converts data into signals for transmission.
It creates the physical connection between devices.
05

## Slide 6
2
LAYER 2 OF 7
Data-Link Layer
L3 data
(from Network)
→
Adds Header (H2)
& Trailer (T2)
→
Frame →
Physical Layer
Main Points
Handles data transfer between devices on the same network.
Divides data into smaller pieces called frames.
Detects and corrects errors during transmission.
Manages physical addressing using MAC addresses.
Responsible for the error-free transfer of data frames.
It ensures data is sent and received without errors.
06

## Slide 7
3
LAYER 3 OF 7
Network Layer
L4 data
(from Transport)
→
Adds Header (H3)
→
Packet →
Data Link Layer
Main Points
Handles routing and forwarding of data between networks.
Uses IP addresses for identifying devices.
Breaks data into packets for transmission.
Finds the best path for data to reach its destination.
Manages logical addressing and routing between networks.
Examples: IP addresses (IPv4, IPv6), routers.
07

## Slide 8
4
LAYER 4 OF 7
Transport Layer
L5 data
(from Session)
→
Segments +
Header (H4) x3
→
L4 data →
Network Layer
Main Points
Ensures reliable data transfer between devices.
Breaks large data into smaller segments for easier handling.
Uses protocols like TCP and UDP to manage data flow.
Guarantees data arrives in the correct order without errors.
Provides end-to-end communication and reliable delivery.
TCP: reliable, connection-oriented.
UDP: fast, connectionless.
08

## Slide 9
5
LAYER 5 OF 7
Session Layer
L6 data
(from Presentation)
→
Adds syn markers
+ Header (H5)
→
L5 data →
Transport Layer
Main Points
Manages sessions/connections between devices.
Controls the start, maintenance, and end of communication sessions.
Keeps track of dialogue (one-way or two-way).
Ensures that data flows smoothly during a session.
Establishes, maintains and synchronizes device interaction.
09

## Slide 10
6
LAYER 6 OF 7
Presentation Layer
L7 data
(from Application)
→
Encode, encrypt,
compress + H6
→
L6 data →
Session Layer
Main Points
Translates data into a format the application can understand.
Handles data encryption and decryption for security.
Manages data compression to reduce size.
Ensures data is in the right format and secure.
10

## Slide 11
7
LAYER 7 OF 7
Application Layer
User
→
X.500 · FTAM · X.400
→
L7 data →
Presentation Layer
Main Points
Directly interacts with user applications (web browsers, email).
Provides services like file transfers, email, and network management.
Facilitates communication between software applications and the network.
A window for users and applications to access network services.
11

## Slide 12
PROS & CONS
Advantages of the OSI Model
1
Standardization
Provides a common reference so different vendors build compatible systems.
2
Modularity
Splits communication into independent, manageable layers.
3
Interoperability
Lets different types of computers and networks work together.
4
Troubleshooting
Issues can be isolated to a specific layer.
5
Scalability
New technologies can be added at a single layer without disrupting others.
12

## Slide 13
PROS & CONS
Disadvantages of the OSI Model
1
Complexity
Seven layers can be harder to learn and apply than simpler models.
2
Not Widely Used
Real-world networks mostly implement the simpler TCP/IP model instead.
3
Oversimplification
Some real protocols don't map cleanly onto a single layer.
4
Does Not Define Protocols
It is only a reference model — it doesn't specify actual protocols to use.
13